## Slide 1
Engr 220 Lab
Calvin College Engineering Department
2022

## Slide 3: Last Week
ASCII Characters & C-Strings
Serial Communication
DE2 Board LCD Device
SignalTap Analyzer
Questions?
No assembly this week

## Slide 4: Pointers in C
Variables have addresses which can be pointed to (remember Lab10)
Pointers can be dereferenced

## Slide 5: Pointers in C
Arrays are similar to pointers to the first element (remember Lab 8)

## Slide 6: Pointers in C
char* is similar to char[], both can be used as strings

## Slide 7: Pointers in C
Online Tutorials
  https://www.tutorialspoint.com/cprogramming/c_pointers.htm
  http://www.geeksforgeeks.org/pointers-in-c-and-c-set-1-introduction-arithmetic-and-array/
  https://www.programiz.com/c-programming/c-pointers
  https://www.cprogramming.com/tutorial/c/lesson6.html

## Slide 8: DE2 UART Device
Another I/O device which is capable of sending and receiving bytes of data
9 pins, 7 data, RX, and TX
https://www.circuitbasics.com/basics-uart-communication/
https://en.wikipedia.org/wiki/RS-232

## Slide 9: DE2 UART Device
Another I/O device which is capable of sending and receiving bytes of data
9 pins, 7 data, RX, and TX
https://www.circuitbasics.com/basics-uart-communication/
https://en.wikipedia.org/wiki/RS-232

## Slide 10: DE2 UART Device
Another I/O device which is capable of sending and receiving bytes of data
9 pins, 7 data, RX, and TX
https://www.circuitbasics.com/basics-uart-communication/
https://en.wikipedia.org/wiki/RS-232

## Slide 11: DE2 UART Device
Another I/O device which is capable of sending and receiving bytes of data
9 pins, 7 data, RX, and TX
https://www.circuitbasics.com/basics-uart-communication/
https://en.wikipedia.org/wiki/RS-232

## Slide 12: UART Serial Communication
DE2 Board UART Device Register Bit-Fields
7-bits of ASCII data provided in time
RAVAIL shows quantity of data remaining, decreases to 0

## Slide 13: UART Serial Communication
DE2 Board UART Device Register Bit-Fields
7-bits of ASCII data provided in time
RAVAIL shows quantity of data remaining, decreases to 0
Implicit data queue (FIFO) is hidden from us, RAVAIL is its size
  What might happen if we publish to queue faster than we consume from it?

## Slide 14: UART Serial Communication
Windows 10 PC
Putty
Altera DM
Software (Loading/Debugging)
Altera DE2 Board
Quartus
FGPA
NIOS Processor Image
(Flashed)
Software (Executing)
NIOS Processor Image
NIOS Processor Image
Peripheral Devices
(Ex: switches, buttons, hex displays)
Switches
Timer
7Seg Displays
LEDs
Keys
UART
LCD
Can debug code &
access mem./dev.s
Q. SignalTap
QST can view
UART traffic & LCD traffic
from signals on “wires”

## Slide 15: DE2 UART Device
Show reference examples
  https://calvincollege-my.sharepoint.com/:v:/g/personal/ajj6_calvin_edu/Ec8zCBIvzV9JhnlDqSoTUOYB6hY3tL6xGzq6SKRyXgZdPg?e=mAnhyd
  https://calvincollege-my.sharepoint.com/:v:/g/personal/ajj6_calvin_edu/EYrKXugFCtRGg6XEoi1rj6gBdhFvdQHWlWG2H98QmUrXsQ?e=j6iMpO
  (Links from 2020)

## Slide 16: Lab 12 Tips
Refer to the LCD reference & example therein
Refer to the UART reference
Take a minute to review Lab 11, Lab 12 is based on Lab 11
Refer to the Lab 11 slide deck for examples of ASCII characters & strings
Use “Program with Device Driver Support” to get the BSP

## Slide 18: Lab Components
Windows 10 PC
Altera DM
Software (Loading/Debugging)
Altera DE2 Board
Quartus
FGPA
NIOS Processor Image
(Flashed)
Software (Executing)
NIOS Processor Image
NIOS Processor Image
Peripheral Devices
(Ex: switches, buttons, hex displays)
Switches
Timer
7Seg Displays
LEDs
Keys

## Slide 19
Compiler-Generated for NIOS: view in debugger, depends on optimization
Assembly Code
We are using these in Engr220 Lab
Altera DE2 FPGA Hardware
We made a system configuration for this FPGA component in Lab 5, it executes our program and can be viewed by the debugger
NIOS Processor Image
Compiler-Generated for NIOS: view in memory, determine from reference
Machine Code
Factorial Prelab: “portable” C-Code
C Code
Compiling
Assembling
Loading
We don’t have these in Engr220 Lab
NIOS Processor Hardware
Loading
Flashed
Refer to Lab 5 Quartus Process & Projects reference slides for more detail

## Slide 20: Char and String Example
/******************************************************************************
Online C Compiler.
Code, Compile, Run and Debug C program online.
Write your code in this editor and press "Run" button to compile and execute it.
*******************************************************************************/
#include <stdio.h>
#include <string.h>
int main()
{
// We looked at printf codes before, %c is for characters %s is for strings
printf( "We will show some examples of characters like '%c' "
"and strings like \"%s\"\n", 'A', "Hi" );
// Here is a character
char letterY = 'Y';
printf( "letterY: %c\n", letterY );
// We can do math on characters, because they are just numbers
char letterZ = ( letterY + 1 );
printf( "letterZ: %c\n", letterZ );
// char* or char[] is an array of characters, meaning a string
char* stringABC = "ABC";
printf( "stringABC: %s\n", stringABC );
// strings must be null-terminated (\0 not shown when hard-coded)
char stringXYZ[4];
stringXYZ[0] = 'X';
stringXYZ[1] = 'Y';
stringXYZ[2] = 'Z';
stringXYZ[3] = '\0';
printf( "stringXYZ: %s\n", stringXYZ );
// string lengths do not usually include the null-terminating char
printf( "stringXYZ is %u in length\n", strlen(stringXYZ) );
return 0;
}
Copy/Paste text from powerpoint into text editor to view

## Slide 21: Pointers Example
/******************************************************************************
Welcome to GDB Online.
GDB online is an online compiler and debugger tool for C, C++, Python, PHP, Ruby,
C#, VB, Perl, Swift, Prolog, Javascript, Pascal, HTML, CSS, JS
Code, is at address 0x%llx with value 0x%llx and size %u\n", &xPtr, xPtr, sizeof(xPtr) );
printf( "xPtr dereferenced is at address 0x%llx with value %d and size %u\n", &(*xPtr), *xPtr, sizeof(*xPtr) );
// array variable y with null-terminated string value "ABC" and 4 elements of size 1-byte
char y[4];
y[0] = 'A';
y[1] = 'B';
y[2] = 'C';
y[3] = '\0';
printf( "y is at address 0x%llx with value %s and size %u\n", &y, y, sizeof(y) );
printf( "y[0] is at address 0x%llx witCompile, Run and Debug online from anywhere in world.
*******************************************************************************/
#include <stdio.h>
int main()
{
// signed variable x with value 5 and size 4-bytes
int x = 5;
printf( "x is at address 0x%llx with value %d and size %u\n", &x, x, sizeof(x) );
// pointer variable xPtr points at variable x
int* xPtr = &x;
printf( "xPtr h value %c and size %u\n", &(y[0]), y[0], sizeof(y[0]) );
printf( "y[1] is at address 0x%llx with value %c and size %u\n", &(y[1]), y[1], sizeof(y[1]) );
printf( "y[2] is at address 0x%llx with value %c and size %u\n", &(y[2]), y[2], sizeof(y[2]) );
printf( "y[3] is at address 0x%llx with value %c and size %u\n", &(y[3]), y[3], sizeof(y[3]) );
// pointer variable yAsPtr points at variable y[0] which is the same as y itself
// unlike y, yAsPtr does not know y's size, but because it is null-terminated the size can be found
char* yAsPtr = &(y[0]);
printf( "yAsPtr is at address 0x%llx with value %s and size %u\n", &yAsPtr, yAsPtr, sizeof(yAsPtr) );
printf( "yAsPtr[0] is at address 0x%llx with value %c and size %u\n", &(yAsPtr[0]), yAsPtr[0], sizeof(yAsPtr[0]) );
printf( "yAsPtr[1] is at address 0x%llx with value %c and size %u\n", &(yAsPtr[1]), yAsPtr[1], sizeof(yAsPtr[1]) );
printf( "yAsPtr[2] is at address 0x%llx with value %c and size %u\n", &(yAsPtr[2]), yAsPtr[2], sizeof(yAsPtr[2]) );
printf( "yAsPtr[3] is at address 0x%llx with value %c and size %u\n", &(yAsPtr[3]), yAsPtr[3], sizeof(yAsPtr[3]) );
// pointer variable yPtr points at variable yAsPtr
char** yPtr = &yAsPtr;
printf( "yPtr is at address 0x%llx with value 0x%llx and size %u\n", &yPtr, yPtr, sizeof(yPtr) );
printf( "yPtr dereferenced is at address 0x%llx with value %s and size %u\n", &(*yPtr), *yPtr, sizeof(*yPtr) );
return 0;
}
Copy/Paste text from powerpoint into text editor to view